## Slide 1
Combined multistage trims for managing of very severe cavitation applications
CONFERENCE
ORGANIZERS

## Slide 2: Combined multistage trims for managing of very severe cavitation applications
Filippo Carlo Bossi | Senior Design Engineer, Ph.D.

## Slide 3: Introduction
When working with high pressure liquid a common valve solution is to use multistage trims to subdived the pressure drop and to contain the flow speed.
Common proposed trim types are:
Multi-path, multi-stage.
Single-path, multi-stage.

## Slide 4: Introduction
Multi-path, multi-stage:
has high number of stages that develop radially but it is limited by the internal diameter of the body
has a single plug that control the flowing area partializing and opening le labyrith sections one by one
the plug need a small gap between the plug and the labyrith stack
Single-path, multi-stage:
the stages develop axially, this limit the stage max number to around 8
all the stages move together giving a continous control of the flow
Both of them has its own benefits and limits:

## Slide 5: Introduction
Single-Path
Multi-Stage
Hybrid-Path
Multi-Stage
Multi-Path
Multi-Stage
Expanding
Cascade
Trim
Tandem
Plug
Limiphon
Additive
Manufacturing
Taking the best of both types

## Slide 6: 1) Risks associated with high Pressure Drop / High Speed: - Examples, Criteria and International standard 2) Case Studies and Previous Experiences: - Analysis and Experiments 3) Current Project: - Modeling of Tandem Plug
CONFERENCE ORGANIZERS
ORGANIZERS

## Slide 7: 1) Risks associated with high Pressure Drop / High Speed: - Examples, Criteria and International standard 2) Case Studies and Previous Experiences: - Analysis and Experiments 3) Current Project: - Modeling of Tandem Plug
CONFERENCE ORGANIZERS
ORGANIZERS

## Slide 8
Typical cavitation and high speed associated damages
Examples

## Slide 9
Physics behind
To reduce the pressure, a valve need to dissipate energy.
Energy dissipation is usually obtained by restriction, expansion and change of direction
The simplest example is the orifice

## Slide 10
Physics behind
Cavitation is a phenomenon correleted with the fluid vapor pressure
When the local pressure goes below the P_vap, gases are released from the liquid phase
The gas bubbles then collapse as the pressure increase

## Slide 11
IEC 60534 approach to cavitation
The IEC criterion need to determine all the required parameters (Xfz, Kc, Fl)
It’s precise, but focus only on cavitation (also on caviation noise…)

## Slide 12
ISA approach to flow speed

## Slide 13
ISA approach to flow speed
<<…
…>>
The ISA criterion trays to answer with a single parameter (K.E.) a variety of problems (see extraction beside)
It is useful and of simple application, but may not be so accurate
Extraction from ISA Control Valve book

## Slide 14
Other approaches to erosion
When solids are entrained into the flow, erosion is much faster then by clean fluid
Different formulations can be found in literature (Reye, Petry, etc..)
Erosion mechanisms are different mainly based on the angle of attack
Abrasion
Direct impact
Parcol has his own formulation for erosion index (I.E.)
Small angle of impact
Plastic deformation / fusion
∆P > 1000 bar
V > 450 m/s
Water Jet

## Slide 15
Best practice solution
The best way to manage all the problems above mentioned is the use of Multi-Stage trims
Subdiving the total pressure drop in smallest ones allows to reduce the speed and the cavitation potetial
The number of stages depends on the established criteria (IEC, ISA, etc…)
P_vap

## Slide 16: 1) Risks associated with high Pressure Drop / High Speed: - Examples, Criteria and International standard 2) Case Studies and Previous Experiences: - Analysis and Experiments 3) Current Project: - Modeling of Tandem Plug
CONFERENCE ORGANIZERS
ORGANIZERS

## Slide 17
Case Study: OTC application
Service conditions:
∆P_max = 258.5 bar
XF_max = 0.9988
Cv_max = 24.9
Cv_min = 0.262
Rangeability = 95
Intermediate cases with:
∆P_ref = 100 bar
XF_ref = 0.65
During start-up, the conditions are extreme!
Frequent start-up and shut down
Case Min
Start-UP
Case Max
Run

## Slide 18
Case Study: trim selection
Standard Limiphon trim
(Multi-Path, Multi-Stages)
5 – PLUG
Material : F6NM nitrided
Hardness : 1000 HV (on the surface only)
1 – FLOW TO OPEN
Flow to open design is used to maximize valve’s Cv, since the flow path area of the limiphon disc stack increases with increasing of the diameter of the disc stack itself.
6 – SEAT
Material : AISI 316 stellited
Hardness : 44 HRC in the contact surface area
50 – LIMIPHON DISC STACK
Material : 1.4913
Limiphon disc stack’s with expansion ratio (increasing of flow passage between inlet and outlet)
56 – CAGE
Material : F6NM nitrided
Hardness : 1000 HV (on the surface only)

## Slide 19
Case Study: first field feedback
Trim got damaged in 3 months
The damage extension was so strong that was impossible to control the minimum flow required
Plug tip and cage holes (closer to the seat - firstly opened at lower travels) where strongly eroded
After laboratory analysis, the cause was mainly identified as cavitation and secondarily by hard particles found in the metal surface (impact erosion)

## Slide 20
Case Study: first design analysis
Since the highest damaged parts where found to be at the first openings, the design analysis was firstly focused on the clearance flow between plug and cage
Valve close
Valve working in the clearance flow
First row fully open

## Slide 21
Case Study: first design analysis
Design Upgrade:
Elimination of cage -> single piece additive manufacturing limiphon stack
Adding more CCF to increase pressure loss
Change of materials:
from F6NM nitrided to INCONEL 718 44 HRC for DISK STACK
from F6NM nitrided to full TCC for PLUG
INCONEL has high Yield Strength and is very though and Age hardening allow the same properties for the whole thickness
TCC is known to be very hard and very high rupture (unfortunately is fragile…)

## Slide 22
Case Study: second field feedback and design analysis
Trim got damaged in 1 month
TCC plug lost almost 1 mm on the external diameter
No significant damages on the limiphon stack (scratches)

## Slide 23
Case Study: second field feedback and design analysis
After CFD analysis:
∆P = 255 bar
The pressure minima were found at the CCF
The peak clearance speed to be 155 m/s!
With cavitation modeling activated
Trim got damaged in 1 month
TCC plug lost almost 1 mm on the external diameter
No significant damages on the limiphon stack (scratches)

## Slide 24
Case Study: second design analysis
Design Upgrade:
Elimination of the CCF
Change of materials:
from full TCC to INCONEL 718 44 HRC for PLUG
07 - stem
11 - adapter
12 - pin
11a - adapter
05 - plug
50 - limiphon pack
06 - seat
14 - gasket
Ugraded to INCONEL 718

## Slide 25
Case Study: second design analysis
Design Upgrade:
Elimination of the CCF
Change of materials:
from full TCC to INCONEL 718 44 HRC for PLUG
The final solution last more than 1.5 year
07 - stem
11 - adapter
12 - pin
11a - adapter
05 - plug
50 - limiphon pack
06 - seat
14 - gasket
Ugraded to INCONEL 718

## Slide 26
Case Study:
experimental investigation
Desing changes:
Adding of equalizing channels -> smoother velocity profile at labyrinth entrance
Reducing the labyrinth section to Øe = 0.8 mm
Equalizing channels
After CFD analysis:
∆P = 280 bar

## Slide 27
Case Study:
experimental investigation
Desing changes:
Adding of equalizing channels -> smoother velocity profile at labyrinth entrance
Reducing the labyrinth section to Øe = 0.8 mm
Equalizing channels
After CFD analysis:
∆P = 280 bar
The peak clearance speed to be 91.3 m/s

## Slide 28
Case Study:
experimental investigation
IETI Testing loop @SIET (Piacenza, ITALY):
∆P = 230 bar
XF = 0.99
Travel = 15% (first labyrinth rows fully open)
Endurance test = 5 continuous days

## Slide 29
Case Study:
experimental investigation
IETI Testing loop @SIET (Piacenza, ITALY):
∆P = 230 bar
XF = 0.99
Travel = 15% (first labyrinth rows fully open)
Endurance test = 5 continuous days
Results:
No damage found
Risk of clogging the small passage areas
Maching of channels and AM repetibilty are critical
Nominal value = 30.67 mm
Nominal value = 30.9 mm
Nominal value = 31 mm

## Slide 30: 1) Risks associated with high Pressure Drop / High Speed: - Examples, Criteria and International standard 2) Case Studies and Previous Experiences: - Analysis and Experiments 3) Current Project: - Modeling of Tandem Plug
CONFERENCE ORGANIZERS
ORGANIZERS

## Slide 31
Current Project: Heat Exchange (experimental)
Service conditions:
∆P_max = 298 bar
XF_max = 0.9988
Cv_max = 0.115
Cv_min = 0.0414
Rangeability = 2.78
Extreme conditions in all cases!
Microflow application!
Requested service life 1 year
Case Min
Case Max

## Slide 32
Current Project: trim selection
Hybrid Multi-Stage Tandem trim -> 2 valves in 1
Main features:
Flow to close to take the advantages of cascade trim
30 labyrinth stages + 5 cascade stages
1 additional disc at outlet (fixed resistance)
3 additional stages granted by the tandem plug
Internals in INCONEL 718 - 44 HRC

## Slide 33
Current Project: modeling of Tandem Plug
Tandem plug has the function to:
increase the number stages when the plug partialized the labyrinth entrance
protect the sealing surface
Tandem plug
Tandem cage
simplifying

## Slide 34
Current Project: modeling of Tandem Plug
Modeling scheme:
The flow paths can be seen a number of resistances in series and parallel
Every elements having its own parameters (Cv, FL, etc…)
Stage
Clearence
Interstage
P_in
Q_in
P_out
Q_out
Conditions:
Q_in = Q_out

## Slide 35
Current Project: modeling of Tandem Plug
Modeling scheme:
Reducing to only one parallel path
Stage
Clearence
Interstage
Node
P_in
Q_in
P_out
Q_out
I1
I2
S1
S2
C2
C1
N0
N3
N1.1
N1.2
N2.2
N2.1
Conditions:
Q_in = Q_out = Q_S1+Q_C1,S2,C2
∆P_N1.1,N2.1 = ∆P_S1 = ∆P_C1,S2,C2

## Slide 36
Current Project: modeling of Tandem Plug
Modeling scheme:
Considering the intermediate path in series
Stage
Clearence
Interstage
Node
P_in
Q_in
P_out
Q_out
I1
I2
S1
S2
C2
C1
N0
N3
N1.1
N1.2
N2.2
N2.1
Conditions:
Q_in = Q_out = Q_S1+Q_C1,S2,C2
∆P_N1.1,N2.1 = ∆P_S1 = ∆P_C1,S2,C2
Cv_series

## Slide 37
Current Project: modeling of Tandem Plug
Modeling scheme:
Grouping the parallel path
Stage
Clearence
Interstage
Node
P_in
Q_in
P_out
Q_out
I1
I2
S1
S2
C2
C1
N0
N3
N1.1
N1.2
N2.2
N2.1
Conditions:
Q_in = Q_out = Q_S1+Q_C1,S2,C2
∆P_N1.1,N2.1 = ∆P_S1 = ∆P_C1,S2,C2
Cv_series
Cv_parallel

## Slide 38
Current Project: modeling of Tandem Plug
Modeling scheme:
Obtaining the full path in series
Stage
Clearence
Interstage
Node
P_in
Q_in
P_out
Q_out
I1
I2
S1
S2
C2
C1
N0
N3
N1.1
N1.2
N2.2
N2.1
Conditions:
Q_in = Q_out = Q_S1+Q_C1,S2,C2
∆P_N1.1,N2.1 = ∆P_S1 = ∆P_C1,S2,C2
Cv_series
Cv_parallel
Cv_series

## Slide 39
Current Project: modeling of Tandem Plug
Validation of the model:
Using CFD on multistage Ball Valve (3 plates)

## Slide 40
Current Project: modeling of Tandem Plug
Effect of varing the clearances on CV

## Slide 41
Current Project: modeling of Tandem Plug
Effect of varing the clearances on CV

## Slide 42
Current Project: modeling of Tandem Plug
Full control of design parameters through modeling
labyrinth
clearance
clearance

## Slide 43
Current Project: Combined modeling of Labyrinth, Cascade and Tandem Plug
Labyrinth Model
Cascade Model
Tandem Plug Model
Hybrid Multi-Stage Tandem Valve

## Slide 44
CONFERENCE ORGANIZERS
ORGANIZERS
Conclusions
When dealing with severe services, pressure drop and velocity must be adequately handled
Choose of proper materials is fundamental
Common severe service multistage trims might not be always adequate
A combination of them can be the best option to:
  Fit the customer’s requirements
  Optimize dimensions and cost

## Slide 45
ORGANIZING SECRETARIAT
Ph. +39 035 3230904
e-mail info@industrialvalvesummit.com
www.industrialvalvesummit.com
CONFERENCE ORGANIZERS
Ph. +39 3474908420
e-mail segreteria@valvecampus.com
www.valvecampus.com
Thanks