## Slide 1
Myths of Leak Detection
CONFERENCE
ORGANIZERS

## Slide 2: Myths of Leak Detection
How misconceptions influence our ways of pressure testing
Arthur Baars | SME Engineered Solutions

## Slide 3: Will it Leak?
Please raise your hand if you believe it leaks

## Slide 4: Why the conditons matter
Forming Gas
Water
Forming Gas again...
Tested @ 11 bar
Hydrogen Leak Detector
Detected – Off the charts...
Tested @ 11 bar
No visual leakage
0,3 bar loss over 2 hours
Tested @ 20 bar
Hydrogen Leak Detector
Leakage started after 15 minutes

## Slide 5: ‘Helium leaks the fastest’
‘Because it has the smallest molecule size’

## Slide 6: Different gas leakages
Viscous - Turbulent
turbulent flow is fluid motion characterized by chaotic changes in pressure and flow velocity.
Viscous - Laminar
laminar flow is characterized by fluid particles following smooth paths in layers
Molecular
Molecular flow is characterized by a free path larger than the area of the test object

## Slide 7: Different gas leakages
Viscous - Turbulent
turbulent flow is fluid motion characterized by chaotic changes in pressure and flow velocity.
Viscous - Laminar
laminar flow is characterized by fluid particles following smooth paths in layers
Molecular
Molecular flow is characterized by a free path larger than the area of the test object
Transitional
A combination of laminar and molecular

## Slide 8: Viscous Flow
Laminar flow - a variation of Hagen Posseuille
η = dynamic viscosity of the gas
l = length of the leak
r = radius of the leak
= pressure in the object
= atmospheric pressure
q = leakrate
K = constant

## Slide 9: Viscous Flow
Laminar flow - a variation of Hagen Posseuille
η = dynamic viscosity of the gas
l = length of the leak
r = radius of the leak
= pressure in the object
= atmospheric pressure
q = leakrate
K = constant
A quick conclusion
Lower viscosity, means bigger leakage.

## Slide 10: Viscous Flow
Laminar flow - a variation of Hagen Posseuille
η = dynamic viscosity of the gas
l = length of the leak
r = radius of the leak
= pressure in the object
= atmospheric pressure
q = leakrate
K = constant
A quick conclusion
Lower viscosity, means bigger leakage.
Gas | Viscosity @25C [10-6 Pa s] | Conversion of Helium Leak rate
Hydrogen | 8.9 | x 2.21
Methane | 11.2 | x 1.76
Nitrogen | 17.9 | x 1.10
Air | 18.3 | x 1.08
Helium | 19.7 | -

## Slide 11: Molecular Flow
Molecular flow - Knudsen
R = universal gas constant
T = Absolute temperature (K)
M = relative mass of molecule
= pressure in the object
= atmospheric pressure
d = diameter of leak
l = length of the leak

## Slide 12: Molecular Flow
Molecular flow - Knudsen
R = universal gas constant
T = Absolute temperature (K)
M = relative mass of molecule
= pressure in the object
= atmospheric pressure
d = diameter of leak
l = length of the leak
A quick conclusion
Lower Molecular Mass, means bigger leakage.

## Slide 13: Molecular Flow
Molecular flow - Knudsen
R = universal gas constant
T = Absolute temperature (K)
M = relative mass of molecule
= pressure in the object
= atmospheric pressure
d = diameter of leak
l = length of the leak
Gas | Molecular Mass | Conversion of Helium Leak rate
Hydrogen | 2 | x 1.41
Helium | 4 | -
Methane | 16 | x 0.50
Nitrogen | 18 | x 0.38
Air | 19 | x 0.37
A quick conclusion
Lower Molecular Mass, means bigger leakage.

## Slide 14: ‘Helium leaks the fastest’
‘Because it has the smallest molecule size’

## Slide 15: What does it mean?
1 - Helium is great for Cryogenics, and level AH and BH Fugitive Emissions
2 - It’s not about the test result.
The procedure guarantees quality
3 – Clever use of different test media can save costs and reduce test times
Shell revised MESC SP 77/312 to allow forming gas for Fugitive Emission Production Testing. Purpose is to save costs
Cycle time for testing of EN-12266 valves can be reduced by more than 75%, AND automatic detection of leaks can actually be guaranteed

## Slide 16: At Ventil we believe it is fundamentally important to rethink our old ways. Right use of technology will bring our industry to a next level, but our standards must allow deployment It is essential to develop production technology and QA/QC procedures to keep up with valve trends. We simply cannot afford to continue without change Now is the time to define a sustainable practice and purpose driven way forwards. It requires dialogue, and it starts here. Today.
CONFERENCE ORGANIZERS
ORGANIZERS

## Slide 17
Get in touch! – abaars@ventil.nl

## Slide 18
ORGANIZING SECRETARIAT
Ph. +39 035 3230904
e-mail info@industrialvalvesummit.com
www.industrialvalvesummit.com
CONFERENCE ORGANIZERS
Ph. +39 3474908420
e-mail segreteria@valvecampus.com
www.valvecampus.com
Thanks