## Slide 1
Electrical Failsafe Actuator on HIPS Surface Safety Valve
CONFERENCE
ORGANIZERS

## Slide 2: Electrical Failsafe Actuator
on HIPS Surface Safety Valve
Syed M. Nisar | Saudi Aramco
Kai Ewald | AUMA Riester

## Slide 3: Agenda
  Introduction
  Brief Background
  Replace Hydraulic System
  Proposed Technology
  Design Scope and Concept
  Operation Method
  Further Possibilities
  Field Pilot
  Realized Benefits

## Slide 4: Introduction
More than 1800 Gas wells
Repetitive hydraulic failures & Spurious trips
CONFERENCE ORGANIZERS

## Slide 5
Brief Background

## Slide 6
Replace Hydraulic System
Hydraulic Power Units & Actuators
Reduce OPEX
  Contamination
  Leaks
  Refills
  Alarms
  Human errors
Increase Reliability
Maintain Safety
Increase Operational Efficiency

## Slide 7
Proposed Technology
Corporate Technical Challenge
Linear Electric Fail-Safe Actuator
First Company in the World

## Slide 8
DESIGN CONCEPT
Replace Hydraulic with Electric
Electric motor to open valve
Mechanical spring-fail-safe to meet safety
Brake to maintain valve open
Modular design
Open against 10,000 psi
Close w/o pressure assistance
IEC Ex d electrical area classification
High temperature rating
Electric Motor
Brake unit
Valve connection
Terminal box
Gearing system
Linear unit

## Slide 9
Electric Motor
Brake unit
Linear unit
Gearing system
Valve bonnet
Spring Unit
DESIGN CONCEPT
Failsafe Electric Actuator

## Slide 10
DESIGN CONCEPT
Actuator
  Motor: Using an existing motor from AUMA portfolio
  Brake unit – two integrated brakes with different functions:
    Holding brake: for locking Fail-Safe-Unit and valve in OPEN (lower) position
    Centrifugal brake, as a speed limiter of the motor speed while closing
Gearbox: non-self-locking gear system

## Slide 11
OPERATION
Open by motor (only)
  Energizing motor
  Opening valve & compressing spring
  Open position feedback via limit switch
  De-energizing motor
  Energizing holding-brake
OPEN

## Slide 12
OPERATION
Close by spring (fail-safe)
  ESD low active signal – releasing holding brake
  Spring moves valve & actuator to CLOSE
  Centrifugal brakes controls
  Close position feedback via limit switch
CLOSE

## Slide 13
Further possibilities
AUMA modular design
  Modular design
  Away up to 100m (high temp or vibration)
  Digitalization IOT ready
  Asset management
  Remote diagnostics
  Predictive Maintenance
  Etc.

## Slide 14: Realized Benefits
  Annual OPEX saving
  CAPEX saving
  Gas well startup time improvement by 93%
  Eliminate downtime of hydraulic failures
  Eliminate oil leaks
  Prevent unwanted risks
  Increase integrity of gas reservoir
  Increase sustainability of production

## Slide 15: Field Pilot
Successfully completed in 2022
Saudi Aramco Engineering Report Issued
CONFERENCE ORGANIZERS

## Slide 16
SYED NISAR
e-mail syed.nisar@aramco.com
KAI EWALD
e-mail kai.ewald@auma.com
Thank You

## Slide 17
ORGANIZING SECRETARIAT
Ph. +39 035 3230904
e-mail info@industrialvalvesummit.com
www.industrialvalvesummit.com
CONFERENCE ORGANIZERS
Ph. +39 3474908420
e-mail segreteria@valvecampus.com
www.valvecampus.com
Thanks