## Slide 1
Numerical investigation on the performance of safety relief valves
CONFERENCE
ORGANIZERS

## Slide 2: Numerical investigation on the performance of safety relief valves
Nicoletta Franchina | Researcher - UniBG

## Slide 3: SRV: direct loaded SRV
SRVs may operate with both compressible and incompressible flows, e.g. in shell-type water-gas heat exchangers
→ Proper valve trim
→ Satisfactory functional characteristics
High resolution CFD computations.
SRV operating under varying conditions and using different gases/fluids.
Exhaust mass flow rate must be ensured – Reliable prediction of the discharge coefficient.
Gases/Fluids characterized by different thermo-ﬂuid-dynamic properties

## Slide 4: Orifice D SRV with air, argon and ethylene
CE-ISO, ASME, ASME PTC25, ISO4126:1 require lab testing to evaluate disc lift and discharge coefficient (%Pset)
Standard procedure: assume the functional and ﬂowing safety valve characteristics as independent of the gas
Petrochemical applications: thermo and fluid-dynamic properties of actual exhausted gas are very different from tests
Topic of investigation:
Flowing characteristic as a function of the flow compressibility
- Discharge
coefficient K
- Actual lift
- Relevant flow
phenomena
Standard procedure: lab tests using air
(not feasible with certain gases/sizes)
Argon & Air exp tests: orifice D 1/2”x1” relative Pset of 4 barg

## Slide 5: Hi-resolution CFD: high-order DG
Discontinuous functional discretization
Proper numerical fluxes must be used at interfaces
Discretization: RANS, realizable k-ω model by Menter; “exact” Godunov-type solution of the Riemann problem & BRMPS; local shock-capturing
PROs: Great flexibility and accuracy; compact num schemes
CONs: Increase in the number of DOFs; high CPU cost
SRV results presented: (k+1)-order accurate solutions (converged up to a L2 norm of residuals lower than 10-5).
Computational grid: 315k elements [half domain]
Standard procedure: lab tests using air
(not feasible with certain gases/sizes)
Finite element discretization
Reynolds number (based on the total upstream conditions and oriﬁce radius) approx 4 106 for both air and argon almost twice this value for ethylene.

## Slide 6: Hi-resolution CFD: high-order DG
Validation: air
Computations: at nominal disc lift, four overall pressure ratios 3,6,10,12 barg
→ from choked throat condition to nearly sonic outlet
ﬂange, for the selected gases
→ Net force acting on the valve stem: well predicted
→ Discharge coefficient: exp trend reproduced though somewhat overestimated
Mach contours at sym plane - P=10barg

## Slide 7: Hi-resolution CFD: high-order DG
Validation: air
→ Complex pattern of shocks and expansion waves takes place inside the body
→ Evolution of streamlines originated at the valve oriﬁce
Total P contours at sym plane - P=10barg

## Slide 8: Hi-resolution CFD
Air, Ar, C2H4
Thrust acting on the bonnet rear part
Discharge coefficient K
→ Increasing the speciﬁc heat ratio: both thrust exerted on the spring and K coefﬁcient decrease
→ Consistent with the outcomes of the Ar exp
K ratio of actual to ideal mass flow rate:

## Slide 9: Hi-resolution CFD
Air, Ar, C2H4
Thrust acting on the bonnet rear part
The critical pressure ratio is greater at higher gamma →At Pt fixed, the static pressure near and before the sonic line is lower thereby reducing the upward thrust on the disc.
Between valve inner volume and exhaust:
Backpressure on the rear of the moving device is also expected to increase with gamma (as it occurs at flange exit)
→ Again lower net opening force
Thrust acting on the bonnet rear part
γ=1.255
γ=1.667

## Slide 10: Hi-resolution CFD
Air, Ar, C2H4
Discharge coefficient: as
composed by the product of
a viscous coefﬁcient and a
geometrical one
→ Compressibility inﬂuences the formation of the vena contracta
→ Increased minimum area at ﬂow disposal in the higher subsonic regimes.
Effect more relevant @ low gamma
Discharge coefficient
γ=1.255
γ=1.667

## Slide 11: Hi-resolution CFD: high-order DG
Water 2”J 3”according to API 526) designed for steam–water double protection
Pressure and velocity contours at sym plane – P=5.89barg - Nominal lift
DG SRV in water (beta=1.5)
DG SRV in water (beta=5.9)
Exp (beta=5.9)

## Slide 12: Hi-resolution CFD: high-order DG
Air 2”J 3”according to API 526) designed for steam–water double protection
Discharge coefficient:
Higher in air
(even in subsonic condition)
→positive compressibility effects
→viscous losses only up to sonic throat
DG SRV in water (beta=1.5)
SRV in air (beta=1.5,5.89)
K air > K water
Air: Mach contours at sym plane – P=1.5barg Nominal lift

## Slide 13: When dealing with gases with γ higher than air: * At the same overpressure the disc lift is reduced due to a decrease of the opening force acting on the disc * The discharge coefﬁcient is lower than expected due to a less favorable compressibility effect on the vena contracta
CONFERENCE ORGANIZERS
ORGANIZERS
Final Remarks 1

## Slide 14: When dealing with gases with lower γ (e.g. steam), both thrust and discharge coefﬁcient are expected to be higher than in air, with no risk in principle for the protected device. Nevertheless, the general increase in thrust can strongly inﬂuence the reclosing pressure implying a higher blowdown rate that might be balanced by a proper adjustment of the setting ring.
CONFERENCE ORGANIZERS
ORGANIZERS
Final Remarks 2

## Slide 15: Discharge coefficient reduction Reduced disc lift due to decreasing opening force Less favorable compressibility effects
2.3%
4%
g4%
2.3%
5.1%
CONFERENCE ORGANIZERS
ORGANIZERS

## Slide 16
ORGANIZING SECRETARIAT
Ph. +39 035 3230904
e-mail info@industrialvalvesummit.com
www.industrialvalvesummit.com
CONFERENCE ORGANIZERS
Ph. +39 3474908420
e-mail segreteria@valvecampus.com
www.valvecampus.com
Thanks