## Slide 1
Fugitive emissions of a valve with gaseous hydrogen
CONFERENCE
ORGANIZERS

## Slide 2: Fugitive emissions of a valve with gaseous hydrogen
Emmanuel Sauger | Cetim, Fluid & Sealing Technologies Department, France
E. Sauger, C. Plumecocq, J. Leray, L. Cougnon
Author:

## Slide 3: Context and objectives of the works
Hydrogen is extremely flammable and forms explosive atmospheres very easily.
Sealing systems are a major factor in safety, equipment reliability and environmental impact control.
To develop a test bench for characterization of fugitive emissions with gaseous hydrogen
To measure fugitive emissions of a standard Oil & Gas valve

## Slide 4: Outlook
1 - Approach and Development of test installation
2 - Test procedure
3 - Test results
4 - Conclusions

## Slide 5: 1 - Approach and Development of test installation

## Slide 6: Approach & test installation
Tested valve
  4’’ Class600 ball valve with Atex IIC actuator
  Equipped to measure leak rate using the vacuum test method
  Stem seal : elastomer O-rings
  Internal metal seal
  Flanges: graphite spiral wound gaskets

## Slide 7: Approach & test installation
P&ID presentation
H2 supply
Pressure control
H2 leak measurement

## Slide 8: Approach & test installation
Safety approach from P&ID
Risk assessment
Test protocol
Safety protocol

## Slide 9: Approach & test installation
Test installation at low temperature
Hydrogen unit
Cooling with LN2
Supply of H2, He and N2
Tested valve
Pressure control panel
H2 booster
H2 mass spectrometer
Thermal enclosure
H2 sensor
Valve installation
Leak rate measurement

## Slide 10: Approach & test installation
Test installation at high temperature
Tested valve
Pressure control panel
H2 Booster
H2 mass spectrometer
Thermal insulation
Leak rate measurements
Valve installation
Atex Heating elements
Hydrogen unit

## Slide 11: 2 - Test procedure

## Slide 12: Test procedure
ISO 15848-1 / CO1 at 150°C and -29°C (FE – H2 mass spectrometer)
Internal tightness (ISO 5208) - H2 Flowmeter
With He before and after test, Preferred Flow Direction (PFD)
With H2 before and after cycling at Tamb, PFD
With H2 at (Test, 50 cycles) and (Test; 205 cycles) Ttest=-29°C or +150°C, PFD
Test at +150°C
Test at -29°C

## Slide 13: Test procedure
Performance class (ISO15848-1) – reminder of classification
Internal tightness (ISO 5208) - criterion
  Tightness Class : AH, BH, CH (H : He; M : methane)  « AH2, BH2, CH2 »
  Endurance: CO1, CO2, CO3 (ON/OFF valve); CC1, CC2, CC3 (control valve)
  Temperature (Ttest at the fluid line )
  Pressure: valve pressure class
  Example of valve classification with helium
    CH - CO1 - SSA 1 - tRT (150°C) – PN100 - ISO 15848-1:2015\Amd.1:2017
  Tightness: rate D (metallic seat)  30 xDN = 30 x 100 = 3 000 mm3.s-1= 180 ml/min
  Problem : unstable leakages + leakages higher than flowmeter range
   pressure stages up to 100 bar and down to Patm.
Notes: It is only a remind of classification and criteria

## Slide 14: 3 - Test results

## Slide 15: Test results
ISO 15848-1 test at -29°C
  Few variation of leak rates  low interfacial leak with this material O-ring
  Performance Class « BH2 »-CO1- SSA0-(t-29°C)-ISO 15848-1:2015\2017

## Slide 16: Test results
Internal tightness test at -29°C
  Increasing pressure: H2-leakage at lower pressure than He-leakage
  depressurisation : H2-leakage / He-leakage is between 2-3
Flowmeter saturation with He
Flowmeter saturation with H2

## Slide 17: Test results
ISO 15848-1 test at 150°C
  Tightness Class « CH2 »  influence of O-ring material permeability at high temperatures
  Performance Class « CH2 »- CO1- SSA0-tRT(+150°C)-ISO 15848-1:2015\2017

## Slide 18: Test results
ISO 15848-1 test at 150°C
  Better tightness behaviour at high temperature and high pressure
  Same kind of variations between H2 and He observed at low temperature
Flowmeter saturation
Flowmeter saturation
(Tamb; 50 cy)
(150°C; 50 cy)
(Tamb; 205 cy)
(150°C; 205 cy)
Hydrogen
Helium
(Tamb; 50 cy)
(150°C; 50 cy)
(Tamb; 205 cy)
(150°C; 205 cy)

## Slide 19: Test results
ISO 15848-1 test at 150°C - Comparison of H2 and He
  It takes more time to perform H2 measurements (safety)
  Same kind of leak rate variations with H2 and He
  Higher leak rates with H2
Hydrogen (100 bar)
Helium (425 bar)

## Slide 20: 4 - CONCLUSIONS

## Slide 21: Conclusions
  Cetim has developed:
    A safety approach to perform H2 test of valves
    A testing facility to measure fugitive emission of H2 at high and negative temperatures
  Test program is carried out on a ball valve
  Fugitive Emission measurements following ISO 15848-1
    Test at -29°C : « BH2 »-CO1- SSA0-(t-29°C)-ISO 15848-1:2015\2017
    Test at +150°C : « CH2 »-CO1- SSA0-tRT(+150°C)-ISO 15848-1:2015\2017
    Same kind of leak rate variation with He and H2. Higher levels of H2 leak rates.
  Internal tightness measurements following ISO 5208
    With the tested valve leaks are much higher than rate D of ISO 5208 at 100 bar
    Difficulties to obtain leak stabilizations
    Ratio H2-leakage / He-leakage is between 2-3
Notes: During this project, Cetim has …

## Slide 22
Thank you for your attention
Do you have any questions ?
Notes: During this project, Cetim has …

## Slide 23
ORGANIZING SECRETARIAT
Ph. +39 035 3230904
e-mail info@industrialvalvesummit.com
www.industrialvalvesummit.com
CONFERENCE ORGANIZERS
Ph. +39 3474908420
e-mail segreteria@valvecampus.com
www.valvecampus.com
Thanks