## Slide 1: Giovanni Bettega
Advanced meshing techniques and their application on complex valve geometry components - Case study on Valves Subcomponents
ORGANIZERS
SCIENTIFIC COMMITTEE
IVS 2022
Technical Conference
Chief Technical Officer @ Solvo srl
Simone Mandelli
General Manager @ Solvo srl

## Slide 2
Biography
Eng. Giovanni Bettega
M.Sc. in Nuclear Engineering at Politecnico di Milano
PhD –Physics at Università degli Studi di Milano
More than 15 years of experience in FEA/CFD simulation, research project and technical consulting \
Eng. Simone Mandelli
M.Sc. in Engineering at Politecnico di Milano
PhD – Civil Engineering at Politecnico di Milano
More than 10 years of experience in FEA/CFD simulation, research project and technical consulting

## Slide 3
Outline
Introduction
  Solvo Srl – Company profile and mission
Criticalities of complex geometry meshing
  Why meshing of valve subcomponents is more and more critical
Case study on Valves Subcomponents
Q&A session

## Slide 4
Introduction

## Slide 5
Solvo Srl is an Italian start-up based in Milan, will provide an innovative software for Finite Element Analysis and all related supporting activities.
MISSION:
SOLVO aims to support partners providing an advanced simulation tool able to guarantee the highest technological level
WHAT WE DO:
The company is developing a software able to perform simulation using a set of Open-Source solvers. The software will be soon released to the market.
Customized software solution
Technical consultancy activities
About us: Company profile

## Slide 6
Criticalities of complex
geometry meshing

## Slide 7
Meshing of critical geometries
Why meshing of valve subcomponents is more and more critical
Valves are more and more subjected to higher pressure or thermal stresses
Pressure up to 20000 psi – Cryogenic or high temperature – Vacuum
New production technics, like Additive manufacturing, are introducing more critical geometries and surfaces
Finite Element Analysis are used more and more to prevent testing failures
Raw material costs are pushing valve manufacturers to guarantee excellent performances with lither valves meaning thinner subcomponents
Some example of critical mashing and boundary layer application

## Slide 8
Application and Example
Thermo-mechanical fatigue / high thermal gradient
Coating
Use meshing to properly capture
Physical phenomena, in these example by means of
Boundary layer

## Slide 9
Boundary Layer application – Example 1
Thermal Shock on desuperheater – Fatigue analysis
Asses the fatigue behavior along the service life according to ASME VIII Div.2
Thermal shock is considered – no gradual transition
Description | Time | Steam |  | Water | 
 | t [min] | T [°C] | Q [kg/s] | T [°C] | Q [kg/s]
Initial condition | 0 | 524.2 | N/A | N/A | N/A
Loading cycle | 1 | 524.2 | 58.48 | 123.8 | 1.27
 | 10 | 524.2 | 58.48 | 123.8 | 1.27
 | 30 | 524.2 | 58.48 | 123.8 | 1.27
Loading cycle on DSH

## Slide 10
Boundary Layer application – Example 1
Thermal Shock on desuperheater – Main boundary conditions
Water flow inside DSH – Convection with cold water
Forced convection with hot steam

## Slide 11
Boundary Layer application – Example 1
Section view – internal mesh
Mesh
Boundary layer used to capture thermal gradient
Prismatic boundary layer with tethadreal mesh (pre-algo with netgen)
4 prismatic layer of 0.5mm
35000 nodes and 188571 elements

## Slide 12
Boundary Layer application – Example 1
Section view – Temperature
Thermal gradient
- Calculation of thermal history until steady state condition is reached

## Slide 13
Boundary Layer application – Example 2
Damage calculation
Stress-strain history analysis for fatigue calculation
Damage index computation through Twice Yield Method
Chart: t [s]
| 0 | 1 | 3 | 5 | 8 | 9 | 10 | 11 | 12 | 14 | 18 | 22 | 30 | 40 | 60 | 160 | 300 | 960
Von Mises Stress | 0 | 78.0764 | 171.539 | 215.875 | 238.453 | 239.779 | 239.385 | 237.764 | 235.285 | 228.742 | 213.706 | 198.988 | 174.542 | 154.065 | 132.389 | 112.119 | 110.814 | 110.774
Hoop Stress | 0 | -72.9036 | -162.421 | -206.309 | -229.897 | -231.602 | -231.597 | -230.362 | -228.263 | -222.421 | -208.523 | -194.66 | -171.348 | -151.59 | -130.699 | -111.634 | -110.411 | -110.374
Section view – Von Mises Stress , Plastic Strain , Damage index

## Slide 14
Boundary Layer application – Example 2
Thermo-mechanical fatigue on casting die
Need to catch high thermal and stress gradient within a small thickness
Boundary layer strategy for obtain a good balance between mesh nodes and computational effort
Very corrupted geometry – no geometric defeaturing used

## Slide 15
Boundary Layer application – Example 2
Mesh – 240444 nodes
Mesh
Boundary layer used to capture thermal gradient
Tetrahedral boundary layer with tetrahedral mesh (Post algo with Tetwild)

## Slide 16
Boundary Layer application – Example 2
Temperature
Thermal analysis
Fatigue calculation:
Thermal cyclic loading
Inner pressure

## Slide 17
Boundary Layer application – Example 3
Seat-Ball contact analysis
Insert coating material on seat and ball
Coating is modeled by a prismatic mesh layer
No need of geometric pre-processing

## Slide 18
Boundary Layer application – Example 3
Coating
Define coating thickness and automatic generation

## Slide 19: Q & A SESSION
ORGANIZERS
SCIENTIFIC COMMITTEE
Thank you for your attention!
IVS 2022
Technical Conference