## Slide 1
THE INTEGRATED VALVE INFORMATION DEVICE FOR EMERGENCY SHUTDOWN VALVE
ORGANIZERS
SCIENTIFIC COMMITTEE
IVS 2022
Technical Conference
ANDREA GIRONI
PAUL TURNER
LGM ENGINEERING - Marketing Manager
IMTEX CONTROLS - CEO

## Slide 2
Biography
Paul Turner
Engineering Director
Imtex controls
Engineering Degree
Paul is a graduate in engineering (Durham University) and joined Imtex in 1995. Paul is the Engineering Director at Imtex, with particular focus on product development and certification at the Company. During his time at Imtex, Paul has managed the development of several new products, some with patented technology and gaining approximately 30 third party product certificates. He has a wide knowledge of the applications that the Company’s products are utilised in and enjoys interacting with clients to develop products and solutions to meet the challenges they face.

## Slide 3
Biography
Andrea Gironi
Marketing Manager
LGM Engineering
Andrea is graduated in Economics (Bocconi University) and joined LGM ENGINEERING in 2018. Andrea started its working experience into a Italian business angel associations, as marketing support in support of startups. Than, he moved to Techogym, operating in the marketing and commercial area. From 3 years, Andrea is formally operating as Marketing Manager in LGM Engineering with particular focus on product marketing and converying to the market innovations and politic to help LGM in expanding is business.

## Slide 4
ORGANIZERS
SCIENTIFIC COMMITTEE
1
WHO WE ARE

## Slide 5
ORGANIZERS
SCIENTIFIC COMMITTEE
2
LGM ENGINEERING

## Slide 6
ORGANIZERS
SCIENTIFIC COMMITTEE
3
IMTEX CONTROLS

## Slide 7
ORGANIZERS
SCIENTIFIC COMMITTEE
IMTEX VALVE COMMUNICATION
Valve Communication & Control Systems
Valve Monitoring
4 to 20mA Position Transmitters
Bus Communication Systems
Valve Diagnostic and Test Systems
CAMTORC ACTUATORS
Pneumatic, Hydraulic and Electro-Hydraulic Actuators
Quarter-Turn and Linear Actuators
Steel, Stainless Steel, Aluminium and Epoxy Construction*
MATIC ACTUATOR SYSTEMS
Valve Automation Service
Site Services
4
IMTEX VALVE COMMUNICATION & ACTUATORS

## Slide 8
ORGANIZERS
SCIENTIFIC COMMITTEE
Two Position - Open or Closed
Must be Automated to Ensure Automatic Response to Emergency Event
Located to Ensure Plant Safety during Potentially Hazardous Events
Inactive for Majority of Operational Life to Maximise Process 'Up' Time
Must 'Fail Safe' on Demand
Integral Part of 'Safety Instrumented System' (SIS) - Final Element
5
OPERATING REQUIREMENTS

## Slide 9
SHUT DOWN VALVE – TYPICAL SCHEMATIC
ORGANIZERS
SCIENTIFIC COMMITTEE
6

## Slide 10
ORGANIZERS
SCIENTIFIC COMMITTEE
Valve becomes stuck or blocked
Deterioration in Actuator Performance
Solenoid fails to release or sticks
THESE PROBLEMS WILL ONLY BE REVEALED WHEN THE SYSTEM IS EXERCISED!
7
TYPICAL PROBLEMS

## Slide 11
SDV ISSUES – IDENTIFICATION METHODS
ORGANIZERS
SCIENTIFIC COMMITTEE
SHUT DOWN EVENT (ESD)
Real-World information
Not desirable to discover a major problem at this time!
FULL STROKE TESTING (FST)
Tests to entire SD system
Usually requires a Plant Shutdown
MUST be performed periodically to comply with FS requirements
PARTIAL STROKE TESTING (PST)
Tests the SD Valve over a specified range
Can be implements without Plant Shutdown
Allows for the interval of FST to be extended
WHEN TESTING, THE GOAL SHOULD BE TO TEST THE VALVE SYSTEM IN A WAY THAT REFLECTS AS CLOSELY AS POSSIBLE THE WAY THE SYSTEM ACTS DURING AN ESD EVENT.
8

## Slide 12
GOAL: INTRODUCE TESTING THAT MIMICS ACTUAL ESD TRIP AS CLOSELY AS POSSIBLE
ORGANIZERS
SCIENTIFIC COMMITTEE
SHUT DOWN VALVE – TYPICAL INSTALLATION
DIAGNOSTIC
CONTROLLER
6
SHUT DOWN VALVE – WITH TESTING DIAGNOSTICS

## Slide 13
VALVESCAN TYPE V SMART CONTROLLER
ORGANIZERS
SCIENTIFIC COMMITTEE
MAJOR BENEFITS
Uses the Solenoid that is part of the ESD Valve Assembly or a Second Solenoid to deliver testing functionality
Works with ANY Solenoid Valve so suits both Hydraulic and Pneumatic Systems
Full Valve Testing (FST/PST/SOT) with Independent Position Monitoring as well as Signatur Capture during Valve Operation
Test Valve, Actuator AND Solenoid
Can work with 1 or 2 Solenoids
Easy to Use for Local, Semi-Local or Remote Control
Easy to Calibrate
Full Diagnostics Available as Standard
Ideal for both New Build AND Retrofit
PRINCIPLE OF OPERATION
Integrate Valve Test Capability into Valve Position Monitor Device that uses the components of the ESD Valve Assembly to deliver the test.

## Slide 14
TYPE V CONTROLLER – OPERATIONAL OVERVIEW
ORGANIZERS
SCIENTIFIC COMMITTEE

## Slide 15
VALVESCAN TYPE V SMART CONTROLLER
ORGANIZERS
SCIENTIFIC COMMITTEE
Fits anywhere a conventional S/Box can be installed
No special Piping required
Utilises any make of Solenoid
Easy to retrofit - downtime 20 minutes

## Slide 16
ORGANIZERS
SCIENTIFIC COMMITTEE
Full Valve Testing (FST/PST/SOT) and ESD Datalogging with up to 4 x Independent Position Monitoring Switches or 2 x Independent 4-20mA Transmitters
IP67 316SS Enclosure with 6 Conduit Entries for flexibility
Integrated Solid State Position Monitor
Communication via HART (VA & VI). Alternative options for Bluetooth and Modbus. (VS only)
Up to 5 x Digital Inputs and 4 x Digital Outputs (typically for Local Control Panel connection)
Up to 2 x Active Analogue Inputs, 1 x Passive Analogue Input and 2 x Analogue Outputs (version dependent)
Solenoid Current Monitoring (VA and VI variants only)
Position and Pressure Monitoring
Onboard Diagnostic Analysis
Optional ‘Automatic’ test feature – device can self initiate tests at regular intervals (in line with IEC 61508 standard recommendation
Multiple Power Options including Loop Powered
Exd (ia) and Ex ib Certified
FEATURES

## Slide 17
ORGANIZERS
SCIENTIFIC COMMITTEE
REMOTE OPERATION
Valve Signature
Partial Stroke Testing
Solenoid Testing
Full Stroke Testing
Valve/Actuator Characteristics – Comparative Analysis
Targeted Fault Finding
Cloud Upload Option (with VDMS)
LOCAL
Local Push Button Initiation
Local Pass/Fail Indicators
Automatic Test Option
TYPE V CONTROLLER – OPERATION & DIAGNOSTICS

## Slide 18
TYPE V CONTROLLER – SIMPLY DATALOGGING FOR ON-OFF VALVES
ORGANIZERS
SCIENTIFIC COMMITTEE
WHAT IF YOU DON’T WANT / NEED TO PERFORM TESTING?
BECAUSE:
Valves are not as critical (Process Control Valves)
Valves operate relatively frequently
Operational Constraints
SOLUTION – TYPE V and VDMS
V-ID Data Logging Solution –Smart Transmitter
Loop Powered Transmitter with Position, Pressure and Solenoid Current Monitoring
Simplified Set-up and Configuration via HART
Simplified data retrieval options including the revolutionary VDMS solution for End-to-End Diagnostics and Monitoring
Local and Cellular Wireless Monitoring with Cloud Analyse

## Slide 19
TYPE V / VDMS IMPLEMENTATION – CONTINUOUS IN-SERVICE VALVE MONITORING
ORGANIZERS
SCIENTIFIC COMMITTEE
3. Plant Safety System and/or Process Control System – No Additional Infrastructure Required at Plant Level as data is shared directly to the cellular network
2. Automated Valve Assembly (Valve, Actuator & Solenoid) equipped with VFMD incl Cellular SIM is put into service and feeds information to Cloud regularly. Benchmarking can be done at this stage (no requirement for the VDMS Plant Master Application)
5. ValveHealth Application to analyse field data and provide real-time information and feedback to key Plant personnel on the health of each automated valve
TEMPORARY HART MODEM CONNECTION
1. VDMS Plant Master Application allows valve ‘As New’ operation data to be logged at FAT and/or First Commission. Shared to ValveHealth Cloud
VALVE INTO SERVICE
Cellular Mast
4. Valve performance raw data harvested directly to Cloud via a Cellular network connection

## Slide 20
ORGANIZERS
SCIENTIFIC COMMITTEE
Retrofit without the need for significant plant modifications
Fully scaleable – Local operation through to full automated condition monitoring solutions
No negative impact on Functional Safety – only the benefit gained from PST implementation
VDMS End-to-End Solution for Datalogging every valve operation WITHOUT affecting Plant Operational Control
SAFETY AND DIAGNOSTIC SOLUTIONS WITHOUT COMPROMISE!!
PARTIAL STROKE TESTING AND VALVE DIAGNOSTICS TAKEAWAYS

## Slide 21: Q & A SESSION Thank you for your attention!
ORGANIZERS
SCIENTIFIC COMMITTEE
IVS 2022
Technical Conference