## Slide 1
STEFANO PINI
Use of the IEC 60870-5-104 protocol in the remote control and management of oil and gas plants, a real case
SW Developer - AiLux
ORGANIZERS
SCIENTIFIC COMMITTEE
IVS 2022
Technical Conference

## Slide 2
Biography – Stefano Pini
UniBS - Electronic Engineering
Started my career in AiLux almost 10 yeas ago
Monitoring systems for oil & gas and electrical substation
Development of network protocols on RTUs
Member of IEC 62351 TC57 – WG15

## Slide 3
Use case: remote control of a Gas Storage Plant
The goals of the project with the new devices are:
Revamping of the remote control equipment of the gas storage plant (RTU and SCADA)
Improved reliability in the data exchanged.
Improved configuration and self-diagnostic
IT security
SCADA

## Slide 4
Device used for remote control of a Gas Storage Plant
CPU with Ethernet Redundancy (4 Ethernet ports)
CPU Redundancy – Hot Swap
CPU with RS232 & RS485
Time Synchronization (IEEE 1588 – Precision Time Protocol)
Power Supply Redundancy
Modularity – In each rack is possible to insert CPU, DI, DO, AI and AO Boards
The Main Rack can be expanded if connected to other Racks – HSR

## Slide 5
Device used for remote control of a Gas Storage Plant
SCADA
Power Supply
Field

## Slide 6
Plant Architecture
The system has been designed without a Single Point of Failure.
Anything that might be affected by a breakdown has a replacement ready to dynamically replace it.

## Slide 7
SCADA communicaton: IEC 60870-5-104 - overview
This network protocol has been designed for the remote control in electric substations.
Has been used also in other fields (e.g. oil & gas) due to the main advantages:
  Interoperability among different vendors
  Support for redundancy
  Data and measures from Controlled Stations to Master Station
  Commands from Master Station to Controlled Stations
  Reliable data (CRC / checksum)
  Low Bandwith required (Minimized protocol overhead)
  Timestamps
  Time synchronization

## Slide 8
SCADA communicaton: IEC 62351 a secure version
of IEC 60870-5-104
IEC Technical Committee 57 – Working Group 15 has been in charge of the security of this protocol (and others).
E2E security by design.
New features:
  Confidentiality
  Mutual Authentication (User/Device Certificates)
  Authenticity
  Integrity
  Role Based Access Control
  Public Key Infrastructure
  Device enrollment

## Slide 9
Field Communication Protocols
The communication with the field equipment is made with this protocols:
OPC-UA
OPC-DA
LonWorks
ModBus-RTU, ModBus-TCP/IP Master & Slave
IEC 60870-5-104 Master/Slave/Reverse/Redundancy + 101 and 103
IEC 61850 Client / Goose & Server
C37.118 Client or Server
IEC 62056-21 (DLMS)
DNP 3
LoRaWAN

## Slide 10
Hardware Cybersecurity
High Assurance Boot:
  Secure Boot
  Trusted Execution
  Cryptographic Accelerators
  Tamper Detection
TPM 2.0 – FIPS 140-2 level 3
  HW Key Protection
AiLux cyber pack: enhanced OT security

## Slide 11
Protocol Certifications
IEC 60870-5-104 ed.2 IEC 62351
IEC 61850 ed.2 in progress

## Slide 12
Hardware Certifications
ENVIRONMENTAL & MATERIAL ELECTRICAL SECURITY SEISMIC

## Slide 13
Web Pages
  RBAC
  Users
  Commands
  Network Parameters
  Protocol Configuration
  System Log
  RTU Status
  Single CPU staus
  Value History
  Configuration Upload

## Slide 14
Configuration

## Slide 15
Q & A SESSION
ORGANIZERS
SCIENTIFIC COMMITTEE
Thank you for your attention!
IVS 2022
Technical Conference
We wait you for a demo – HALL C stand 97
info@ailux.eu