## Slide 1: Stefano Crippa
Tenaris Products for Energy Transition
Tenaris Product Manager • TENARIS Pipeline Technology Division
ORGANIZERS
SCIENTIFIC COMMITTEE
IVS 2022
Technical Conference

## Slide 2
Biography
– Stefano Crippa –
Line Pipe Product Manager for the Pipeline Pipeline Technology Division [Dalmine (BG), Italy]
Academic background: Master Degree in Mechanic Engineering [Politecnico di Milano, Italy]
Working for 14 years in Tenaris, of which 12 years in the current department.
Responsible for analyzing the technical feasibility of the Line Pipe & Bends for Caspian markets. Responsible of the team of engineers analyzing the technical feasibility of the TSH Blue®Riser Connection and providing support to the commercial area in analyzing offerings to meet customer’s quality demands. Develops new special products to meet customers quality demands. 6 Publications in International Journals and Conferences.

## Slide 3
How it will look like
What Everybody Already Know
Source: DNV – Hydrogen - Decarbonising Heat 2020

## Slide 4
PATHWAY TO NET ZERO (PNZ)
Source: DNV – DNV_Pathway_to_net-zero_2021
In order to achieve net zero emissions in 2050, fossil fuel use is reduced about 80% from today, and carbon capture and removal removes a further 8 Gt of CO2 emissions. The 2050 PNZ energy system will be dominated by solar and wind generated electricity, but also sees a strong role for hydrogen in the hard-to-abate sectors.

## Slide 5
PIPELINES FOR LOW-CARBON GASES
Source: DNV – Technology_Progress_Report_2021
The DNV ETO and the International Energy Agency forecast CCUS demand in 2050 will be roughly 100 times larger than collective capacity of the approximately 6,500 km of CO2 pipelines that exist today.
Key considerations for new and repurposed hydrogen and CO2 pipelines
 | Repurposed | New
CO2 | • The design pressure & temperature of the pipeline (avoiding the two-phase region) • Impurities in the CO2 changing fracture propagation properties • Water dew point in the pipeline. • Dense phase CO2 acting as a solvent (elastomer effects) • Fatigue/cycling effects • Life extension of pipelines • Blowdown/venting provisions • Cleaning/purging of existing lines | • Pipeline routing and permitting. • Operating mode (gaseous, liquid or supercritical) and mass density • Public consultation • Possible cryogenic effects • Pressure maintenance (boosting for long pipelines) • Startup/shutdown impacts • Metering • Pipeline sectioning • Linepipe selection

## Slide 6
Market introduction
June 2021 (link)
Tenaris is introducing THera™, at the Carbon Capture & Hydrogen Technology Expo Europe in Bremen, Germany
- Official launch -
October 2021 (link)
THera™, Tenaris Hydrogen era presented at Enlit Europe in Milan
December 2021 (link)
Article & form to request the document :
Tenaris Products for Energy Transition

## Slide 7
Tenaris Products for Energy Transition
Main pending technical issues :
Corrosion / Effects of impurities: typically generated in power plants, such as SOx, NOx, O2, H2S, and C particulates. The main tread remaining CO2-corrosion (water contamination). Need of Stress Corrosion Cracking and Weight Loss validations.
Joule-Thomson effect and vaporization of CO2 : they occur during shutdowns, start-ups or transient operations, and are mainly critical during depressurizing, release or leakage of CO2, causing cooling of the metal and brittle fracture.
Gaps Related to Equations of State - Running Cracks: Verification of reliable equations of state for supercritical CO2.
Main pending technical issues
Liquide CO2 Leakage

## Slide 8
CO2 transportation in pipelines for industrial purposes is not new, but is gaining momentum due to global warming and carbon emissions target (>30 projects under development).
Tenaris Products for Energy Transition
CCS WW Project Overview

## Slide 9
CO2 transportation in pipelines for industrial purposes is not new, but is gaining momentum due to global warming and carbon emissions target (>30 projects under development).
Tenaris Products for Energy Transition
CCS EU Project Overview
Source: Global CCS Institute and IOGP Data

## Slide 10
Project Description:
Development of a full-scale CCS facility on the Norwegian Continental Shelf (NCS). The project will compress and store CO2 captured from industrial sites: Fortum Oslo Varme’s waste-to-energy facility in Oslo and Norcem’s cement factory in Brevik. Liquid CO2 will be transported by ship from the capture facilities to a receiving terminal in Øygarden. CO2 will be transferred from the ship to intermediate storage tanks, prior to being sent through a pipeline on the seabed to injection wells for permanent storage in depleted reservoirs.
Equinor – Northern Lights CCS
2020
2024
2021
FID
PO
2022
2023
Delivery
Installation
Start-up
Tenaris Line Pipe scope:
OD: 12’’
Volume: approx. 12,8 ThTn / 105 Km
Material grade: DNVGL SMLS 450 SFPD
Final delivery (bare pipe): by June 2022
Coating: AC coating (EPC responsibility)
Production Mill: Dalmine

## Slide 11
TENARIS

## Slide 12
TENARIS

## Slide 13: Q & A SESSION
ORGANIZERS
SCIENTIFIC COMMITTEE
Thank you for your attention!
IVS 2022
Technical Conference